## Slide 1: Effect of Intravascular Ultrasound-Guided vs. Angiography-Guided Everolimus-Eluting Stent Implantation: the IVUS-XPL Randomized Clinical Trial
Myeong-Ki Hong, MD. PhD
on behalf of the IVUS-XPL trial investigators
Severance Cardiovascular Hospital and Cardiovascular Research Institute, Yonsei University College of Medicine, Seoul, Korea
Embargoed Until 10:45 a.m. ET, Tuesday, Nov. 10, 2015

## Slide 2: Clinical usefulness of IVUS
Improved clinical outcomes
IVUS usage during PCI
There are no adequately powered randomized clinical trials to prove the clinical usefulness of IVUS for second-generation DESs.
Background
The clinical outcomes of IVUS-guided second-generation DES implantation would be superior to those of angiography-guided DES implantation in a subset of patients with long coronary lesions.
Hypothesis

## Slide 3: Study Design
A prospective, randomized, multi-center trial
At 20 centers in Korea
Enrollment period: Oct 2010 and July 2014
Key inclusion criteria
  Age 20 years or older
  Patients with typical chest pain or evidence of myocardial ischemia
  Non-emergent conditions
  Stent length ≥ 28 mm based on angiographic estimation
  Significant coronary artery stenosis (>50% based on visual estimate) considered for coronary revascularization with stent implantation
Key exclusion criteria
  Acute ST-segment elevation or MI within 48 hours
  Age >80 years
  Cardiogenic shock
  Left ventricular ejection fraction <40%
  Left main disease requiring PCI
  Bifurcation lesion with 2-stent technique
  Chronic total occlusion
  Presence of previously implanted DES within 6 months
  In-stent restenosis lesion

## Slide 4: Study Design
DES implantation with
IVUS guidance
n = 700
DES implantation with
angiography guidance
n = 700
Patients with long coronary lesions
(Implanted stent ≥28 mm in length)
N = 1400
Clinical follow-up at 12 months
Primary end point: MACE
Cardiac death, target-lesion related MI, and ischemia-driven TLR
Clinicaltrial.gov Identifier: NCT01308281
Trial Registration: clinicaltrial.gov Identifier: NCT01308281

## Slide 5: Statistical Analysis
Sample size calculation
  Assumption the overall incidence of MACE to be 7% at the 1-year in the angiography-guidance arm.
  Superiority comparison with an expected risk reduction of 50% in the IVUS-guidance arm (α=0.05, β=0.8, drop-out=5-10%)
  Each 700 patients in the IVUS guidance arm and in the angiography guidance arm.
Primary analysis
  Intention-to-treat analysis with cumulative incidences of MACE at 1 year using the Kaplan-Meier estimates.
  Comparison using the log-rank test.
Turco MA, et al. JACC Cardiovasc Interv. 2008;1:699-709
Kim YH, et al. Circulation. 2006;114:2148-2153

## Slide 6: Procedure
Criteria for stent optimization
  IVUS-guidance arm
    Minimal lumen CSA > lumen CSA at distal reference segments
  Angiography-guidance arm
    Angiographic residual diameter stenosis <30% and the absence of angiographically detected dissection

## Slide 7: Study Flow
670 30 3 34 | Underwent angiography-guidance PCI as randomized Underwent IVUS-guidance PCI Withdrew consent Lost to follow-up
678 22 4 36 | Underwent IVUS-guidance PCI as randomized Underwent angiography-guidance PCI Withdrew consent Lost to follow-up
700 | Included in primary analysis
700 | Included in primary analysis
700 | Randomized to undergo IVUS-guidance PCI
700 | Randomized to undergo angiography-guidance PCI
11972 Excluded
13372 | Patients underwent coronary angiography during the study inclusion period
1400 Randomized
22 8 | Physician preference in complex lesions Angiographically ambiguous anatomy
5 17 | Technical failure to deliver IVUS catheter Physician decision due to unfavorable coronary anatomy

## Slide 8: Baseline Characteristics
Characteristics | IVUS-guidance | Angiography-guidance | P value
No. of patients | 700 | 700 | 
Age, y | 64 (9) | 64 (9) | .54
Male sex | 483 (69) | 481 (69) | .91
Hypertension | 454 (65) | 444 (63) | .58
Diabetes mellitus | 250 (36) | 256 (37) | .74
Left ventricular ejection fraction, % | 62.9 ± 9.8 | 62.4 ± 10.2 | .33
Clinical presentation |  |  | .36
Stable angina | 358 (51) | 356 (51) | 
Unstable angina | 242 (35) | 226 (32) | 
Acute myocardial infarction | 100 (14) | 118 (17) | 
No. of treated lesions per patients | 1.34 (0.56) | 1.36 (0.57) | .57
Duration of DAPT, days | 365 (180, 365) | 365 (180, 365) | .15
Coronary arteries |  |  | .14
Left anterior descending artery | 455 (65) | 419 (60) | 
Left circumflex artery | 96 (14) | 108 (15) | 
Right coronary artery | 149 (21) | 173 (25) | 
Baseline QCA data |  |  | 
Reference vessel diameter, mm | 2.89 ± 0.45 | 2.85 ± 0.45 | .13
Minimum lumen diameter, mm | 0.83 ± 0.42 | 0.82 ± 0.43 | .56
Diameter stenosis, % | 71.1 ± 14.3 | 71.4 ± 14.4 | .70
Lesion length, mm | 34.7 ± 10.8 | 35.2 ± 10.5 | .41
Stent length, mm | 39.3 ± 13.1 | 39.2 ± 12.3 | .90

## Slide 9: Angiographic and Procedural Characteristics
Characteristics | IVUS-guidance | Angiography-guidance | P value
Adjunct post-dilatation | 534 (76) | 402 (57) | <.001
Final balloon size, mm | 3.14 ± 0.43 | 3.04 ± 0.42 | <.001
Overlapping stent | 145 (21) | 138 (20) | .64
No. of stents per lesions | 1.3 (0.5) | 1.3 (0.5) | .48
Stent edge dissections | 15 (2) | 13 (2) | .70
Coronary perforation | 0 | 0 | 1.00
Maximal inflation pressure, atm | 16.5 ± 4.1 | 15.9 ± 4.1 | .052
Post-intervention QCA data |  |  | 
Reference vessel diameter, mm | 3.03 ± 0.44 | 2.97 ± 0.43 | .01
Minimum lumen diameter, mm | 2.64 ± 0.42 | 2.56 ± 0.39 | <.001
Diameter stenosis, % | 12.79 ± 8.66 | 13.74 ± 8.05 | .04

## Slide 10: Clinical outcomes at 1 year
 | IVUS- guidance (n=700) | Angiography- guidance (n=700) | Hazard ratio (95% CI) | Log-Rank P value
Primary End Point |  |  |  | 
MACE | 19 (2.9%) | 39 (5.8%) | 0.48 (0.28–0.83) | .007
Secondary End Point |  |  |  | 
Cardiac death | 3 (0.4%) | 5 (0.7%) | 0.60 (0.14-2.52) | .48
Target lesion related MI | 0 | 1 (0.1%) | - | .32
Ischemia-driven TLR | 17 (2.5%) | 33 (5.0%) | 0.51 (0.28-0.91) | .02
Stent thrombosis | 2 (0.3%) | 2 (0.3%) | 1.00 (0.14-7.10) | 1.00
Acute | 1 (0.1%) | 1 (0.1%) | - | -
Sub-acute | 1 (0.1%) | 0 | - | -
Late | 0 | 1 (0.1%) | - | -

## Slide 11: Primary End Point
0
2
4
6
0
3
6
9
12
Time Since Randomization, mo
No. at risk
Angiography arm
IVUS arm
700
700
673
671
660
665
624
641
643
654
Angiography-guidance
IVUS-guidance
HR, 0.48 (95% CI, 0.28-0.83)
Log-rank P = .007
5.8%
2.9%
Patients with Primary
End Point Event, %

## Slide 12: Post-intervention IVUS analysis in subgroup of IVUS guidance
Procedural and IVUS Characteristics | Patients meeting the IVUS criteria | Patients not meeting the IVUS criteria | P value
No. of patients | 363 | 315 | 
Adjunct post-dilatation | 282 (78) | 237 (75) | .34
Final balloon size, mm | 3.15 ± 0.45) | 3.13 ± 0.42 | .52
Maximal inflation pressure, atm | 16.5 ± 3.9 | 16.4 ± 4.4 | .87
Proximal reference EEM area, mm2 | 17.52 ± 5.34 | 17.27 ± 5.04 | .56
Proximal reference lumen area, mm2 | 9.02 ± 3.51 | 8.86 ± 3.27 | .57
Minimal lumen area, mm2 | 6.09 ± 1.91 | 5.71 ± 1.71 | .008
Distal reference EEM area, mm2 | 9.44 ± 3.98 | 10.94 ± 3.83 | <.001
Distal reference lumen area, mm2 | 5.55 ± 1.82 | 6.83 ± 1.68 | <.001

## Slide 13: Primary End Point
0
2
4
6
0
3
6
9
12
Time Since Randomization, mo
No. at risk
Not meeting the criteria
Meeting the criteria
315
363
299
362
297
345
285
334
394
338
HR, 0.31 (95% CI, 0.11-0.86)
Log-rank P = .017
4.6%
1.5%
Patients with Primary
End Point Event, %
Patients meeting the IVUS-criteria
for stent optimization
Patients not meeting the IVUS-criteria
for stent optimization

## Slide 14: Conclusions
Among patients requiring long coronary stent implantation, the use of IVUS-guidance for DES implantation was associated with a significant 2.9% absolute reduction and 48% relative reduction in the risk of MACE at 1 year, compared with angiography-guidance.
Our findings suggest better clinical outcomes of MACE with IVUS-guidance compared to angiography-guidance for DES implantation, particularly for diffuse long lesions.

## Slide 15
Dreams will
come true